## Slide 1: Arduino programs
Arduino toolchain
Cross-compilation
Arduino sketches
Classes
Sketch structure
Pins
Input and output
Blink example

## Slide 2: Arduino toolchain

## Slide 3: Verify and upload
Combine & transform
Compile
Link
HEX file creation
Code
Libraries
HEX
Upload

## Slide 4: Combine and transform
All program files are combined into one
An #include is added to reference basic Arduino libraries
Function prototypes are added
A main() function is created

## Slide 5: Cross-compilation

## Slide 6: Compile and link
avr-gcc is invoked to cross-compile the code
Resulting code executes on AVR, not on Intel
Generates an object file (.o)
Object file is linked to Arduino library functions

## Slide 7: Hex file creation and programming
Avr-objcopy is invoked to change the format of the executable file
A .hex file is generated from the .elf file

## Slide 8: Arduino sketches

## Slide 9: Arduino programs
A program is called a sketch
C++ program using Arduino library functions
C++ is a superset of C
  All C programs are legal C++
C++ also includes classes

## Slide 10: Object-oriented programming
Organize your code through encapsulation
Group together data and functions that are related
User-defined type is specific to an application
  int type has data (the number) and functions (+, -, *)

## Slide 11: Encapsulation example
Specify and operate on 3 points
int x1, y1; point p1;
x1=0; y1=0; p1.setpoint(0,0);
plot(x1,y1); p1.plot();
All data contained in one objects
Reduced number of parameters
Point-specific functions are easily identified

## Slide 12: Classes

## Slide 13: Classes and members
class X {
public:
int m;
int mf(int v){int old=m; m=v; return old;}
};
X var;
var.m=7;
int z = var.mf(9);

## Slide 14: Classes and members
Declaration of a variable creates an object
. operator used to access members
  Data and functions
Functions can be defined inside the class

## Slide 15: Classes in libraries
We will
  not need to know much about classes
  not define classes
  use classes defined in libraries
Examples
  Ethernet.begin(mac)
  Serial.begin(speed);
  client.print(“Hello”);
  Serial.print(“Hello”);

## Slide 16: Sketch structure

## Slide 17: setup() function
A sketch does not have a main() function
Every sketch has a setup() function
  Executed once when Arduino is powered up
  Used for initialization operations
  Returns no value, takes no arguments
  void setup() {
  …
  }

## Slide 18: loop() function
Every sketch has a loop() function
  Executed iteratively as long as the Arduino is powered up
  loop() starts executing after setup() has finished
  loop() is the main program control flow
  Returns no value, takes no arguments
  void loop() {
  …
  }

## Slide 19: Pins

## Slide 20: Pins
Pins are wires connected to the microcontroller
Pins are the interface of the microcontroller
Pin voltages are controlled by a sketch
Pin voltages can be read by a sketch
Digital I/O
Analog inputs

## Slide 21: Output pins
Output pins are controlled by the Arduino
  Voltage is determined by your sketch
  Other components can be controlled through outputs

## Slide 22: Input pins
Input pins are controlled by other components
  Arduino reads the voltage on the pins
  Allows it to respond to events and data

## Slide 23: Digital vs. analog
Some pins are digital-only
  Read digital input, write digital output
  0 volts or 5 volts
Some pins can be analog inputs
  Can read analog voltages on the pin
  Useful for analog sensors
Analog-only pins are clearly labeled
No pins can generate an analog output

## Slide 24: Input and output

## Slide 25: Input/output (I/O)
These functions allow access to the pins
void pinMode(pin, mode)
Sets a pin to act as either an input or an output
pin is the number of the pin
  0-13 for the digital pins
  A0-A5 for the analog pins
mode is the I/O mode the pin is set to
  INPUT, OUTPUT, or INPUT_PULLUP
  INPUT_PULLUP acts as input with reversed polarity

## Slide 26: Digital input
int digitalRead(pin)
  Returns the state of an input pin
  Returns either LOW (0 volts) or HIGH (5 volts)
Example
  int pinval;
  pinval = digitalRead(3);
  pinval is set to the state of digital pin 3

## Slide 27: Digital output
void digitalWrite(pin, value)
  Assigns the state of an output pin
  Assigns either LOW (0 volts) or HIGH (5 volts)
Example
  digitalWrite(3, HIGH);
  Digital pin 3 is set HIGH (5 volts)

## Slide 28: Analog input
int analogRead(pin)
  Returns the state of an analog input pin
  Returns an integer from 0 to 1023
  0 for 0 volts, 1023 for 5 volts
Example
  int pinval;
  pinval = analogRead(A3);
  pinval is set to the voltage on A3 (0 for 0 volts, 1023 for 5 volts)
  The pin must be an analog pin

## Slide 29: Blink example

## Slide 30: Delay
void delay(msec)
  Pauses the program for msec milliseconds
  Useful for human interaction
Example
  digitalWrite(3, HIGH);
  delay(1000);
  digitalWrite(3,LOW);
  Pin 3 is HIGH for 1 second

## Slide 31: Blink example
Blink is the generic simple example for embedded systems
  Like “hello, world”
FileExamples01.BasicBlink
Causes an LED to blink
LED is built-in, so no wiring required
Connected to pin 13

## Slide 32: Blink sketch
void setup() {
pinMode(13, OUTPUT);
}
void loop() {
digitalWrite(13, HIGH);
delay(1000);
digitalWrite(13, LOW);
delat(1000);
}

## Slide 33: Lab

## Slide 34: State change detection example
Connect to Tinkercad at http://tinkercad.com and log-in.
Go to Circuits and click “Create new circuit” button.
Drag-and-drop the State change detection example from “Arduino””State change detection”.
Examine the code and guess what it does.
Start simulation to check if your guess was correct.
  It counts the number of button press and turns on the built-in LED at every 4 presses.

## Slide 35: Neopixel example
Connect to Tinkercad at http://tinkercad.com and log-in.
Go to Circuits and click “Create new circuit” button.
Drag-and-drop the Neopixel example from “Arduino””Neopixel”.
Examine the code and guess what it does.
Start simulation to check if your guess was correct.
  It sequentially turns on the Neopixel LEDs with randomly varying colors.

## Slide 36: Neopixel with a button
Combine “State change detection” and “Neopixel” to have your simulator do the following.
  When your Arduino is turned on, the Neopixel is sequentially turned on with random colors.
  Neopixel color changes when the number of button press increases (that is when the button status changes from “Released” to “Pushed”).