## Slide 1: Arduino Environment
Arduino platform
Arduino board
Direct programming
Arduino schematics
Arduino IDE
Compiling code
Arduino shields libraries
Arduino basic setup
Arduino simulators

## Slide 2: Arduino platform

## Slide 3: Arduino

## Slide 4: Arduino applications

## Slide 5: Arduino applications

## Slide 6: Arduino applications

## Slide 7: Arduino environment
A development board
  8-bit microcontroller
  Programming hardware
  USC programming interface
  I/O pins

## Slide 8: Arduino environment
A software environment
  Cross-compiler
  Debugger
  Simulator
  Programmer

## Slide 9: Arduino environment
Special-purpose “shields”
  Daughter boards
  Unique functionalities
  Easy to attach
  Good libraries provided

## Slide 10: Arduino board

## Slide 11: The Arduino development board
Has a microcontroller and USB interface to a PC
Large open source community

## Slide 12: Power/Reset
Reset button
USB connector
Power connector

## Slide 13: Input/Output pins
Power/reset pins
Digital I/O pins
Analog input pins
Digital I/O
Power/reset pins
Analog inputs

## Slide 14: Microcontrollers
Main processor
  ATmega328 processor programmed by the user
USB com. processor
  ATmega16U2 handles USB communication
ATmega16U2
ATmega328

## Slide 15: Microcontroller
Microcontroller | ATmega328
Operating voltage | 5V
Input voltage (recommended) | 7-12V
Input voltage (limits) | 6-20V
Digital I/O pins | 14 (of which 6 provide PWM output)
Analog input pins | 6
DC current per I/O pin | 40mA
DC current for 3.3V pin | 50mA
Flash memory | 32KB (ATmega328) (of which 0.5KB used by bootloader)
SRAM | 2KB (ATmega328)
EEPROM | 1KB (ATmega328)
Clock speed | 16MHz

## Slide 16: Firmware
Two types of code executing on a simple microcontroller
  Application code
    Executes the system’s main functionality
    We write this code
  Firmware
    Low-level code: supports the main function
    USB interface, power modes, reset, etc.
  The distinction is a matter of perspective
  Arduino-firmware is pre-programmed

## Slide 17: Direct programming

## Slide 18: Bootloader
Firmware on a microcontroller
Allows the Flash and EEPROM to be programmed
Manages USB communication since application programming is via USB

## Slide 19: In-Circuit Serial Programming (ICSP)
A special programming method to program the firmware
Needed because the bootloader cannot reprogram itself
One ICSP header for each processor

## Slide 20: Arduino schematics

## Slide 21: Arduino UNO schematic
Arduino designs are open source
Design is available
You can build your own

## Slide 22: Microcontrollers and I/O
Power pins
Analog in
Digital I/O
ATmega328
ATmega16U2

## Slide 23: USB, Power, ICSP
Power connector
ICSP2
ICSP 1
ATmega328
ATmega16U2
USB connector

## Slide 24: Arduino IDE

## Slide 25: Arduino IDE
Arduino IDE (Integrated Development Environment)
Menus with all commands
Buttons with common commands
Text editor for writing code
Message area

## Slide 26: Arduino IDE
Button | Function
Verify | Compiles code, checks for errors
Upload | Compiles code, checks for errors, uploads to board
New | Creates a new sketch
Open | Opens an existing sketch
Save | Saves your sketch to a file
Serial Monitor | Opens a window to communicate with the board

## Slide 27: Compiling code

## Slide 28: Compiling code
Verify and Upload both compile
Messages window will show either completion message or error messages
Error messages will show line numbers

## Slide 29: Serial monitor
Displays serial data sent from the Arduino
Allows serial data to be sent to the Arduino from the keyboard
Library functions in the serial library

## Slide 30: Arduino shields and libraries

## Slide 31: Arduino shields
Add-on boards that interface with another device/IC
Can be stacked directly on top of the Arduino
Libraries exist to make interfacing simple
Open source hardware, but most can be purchased
Large variety of shields available
Big advantage of the Arduino platform
Fairly complete list is at http://shieldlist.org

## Slide 32: Some Arduino shields
IMU shields:
Measures 6DOF motion
(acceleration and rotation)
Synthesizer shields:
Generates music
Connects to speaker
Ethernet shields:
Interfaces to Ethernet controllers
Builds web servers/clients

## Slide 33: Arduino basic setup

## Slide 34: Set up the Arduino IDE
Download the IDE
  Easiest to run Windows Installer (http://www.arduino.cc)
  Also installs USB and other drivers
Connect the board to your computer
  Use USB cable
Launch the Arduino application
  Starts the IDE

## Slide 35: Launch the Arduino IDE
Open the Blink example
  FileExamplesBasicsBlink

## Slide 36: Run a program
Select your Arduino
  ToolsBoard menu
Select your serial port
  ToolsPort menu
  There should be only one selection (COM3, etc.)
Upload the program with the upload button
  This writes the program onto the Flash of the Arduino
The LED near pin 13 of the Arduino should blink

## Slide 37: Arduino simulators

## Slide 38: Tinkercad: Circuits
Tinkercad
  http://tinkercad.com
  A free online collection of software tools that help people create and make
  Simulates Arduino circuits and programs with a bunch of electronic components, sensors and actuators
  A good way to test your idea before you actually build

## Slide 39: Tinkercad: Circuits

## Slide 40: Lab

## Slide 41: Blink example
Set up the Arduino development environment
Load the Blink example.
Compile, download, and run.
Modify blink intervals and check if it really works.

## Slide 42: Tinkercad
  Go to http://tinkercad.com
Register for your own account.
Try several Arduino starter examples.
Modify some codes, and check if it works.