## Slide 1: Debugging
Debugging
Debug environments
Debug via serial

## Slide 2: Debugging

## Slide 3: Debug and trace
Controllability and observability are required
Controllability
  Ability to control sources of data used by the system
  Input pins, input interfaces (serial, Ethernet, etc.)
  Registers and internal memory
Observability
  Ability to observe intermediate and final results
  Output pins, output interfaces
  Registers and internal memory

## Slide 4: I/O access is insufficient
Observation of I/O is not enough to debug
If Pin2 is incorrect, how do we locate the bug?
main(){
x=f1(pin1,pin2)
foo(x);
}
foo(x){
y=f2(x);
bar(y);
}
bar(y){
pin3=f3(y);
}
Pin1
Pin2
Pin3

## Slide 5: Properties of a debugging environment
Run control of the target
  Start and stop the program execution
  Observe data at stop points
Real-time monitoring of target execution
  Non-intrusive in terms of performance
Timing and functional accuracy
  Debugged system should ac like the real system

## Slide 6: Debug environments

## Slide 7: Remote debugger
Frontend running on the host
Debug monitor hidden on target
  Typically triggered when debug events occur
  Hitting a breakpoint, receiving request from host, etc.
Debug monitor maintains communication link
Host
Target
Communication link

## Slide 8: Remote debug tradeoffs
Advantages
  Good run control using breakpoints to stop execution
  Debug monitor can alter memory and registers
  Perfect functional accuracy
Disadvantages
  Debug interrupts alter timing so real-time monitoring is not possible
  Need a spare communication channel
  Need program in RAM to add breakpoints

## Slide 9: Embedded debug interfaces
Many modern processors include embedded debug logic
  Embedded trace macrocell (ARM)
  Background debug mode (Freescale)
Debug logic permanently build into the processor
A few dedicated debug pins are added

## Slide 10: Debug and trace features
Breakpoints, stopping points in the code
Watchpoints, memory locations which trigger stop
On-the-fly memory access
Examine/change internal processor values
Single-step through the code
Export softeware-generated data (printf)
Timestamp information for each event
Instruction trace (special purpose HW needed)

## Slide 11: Debug via serial

## Slide 12: Serial protocols
Data is transmitted serially
  Only 1 bit needed (plus common ground)
Parallel data transmitted serially
Original bytes/words regrouped by the receiver
Many protocols are serial to reduce pin usage
  Pins are precious

## Slide 13: UART
Universal asynchronous receiver/transmitter
Used for serial communication between devices
UART is asynchronous; no shared clock
Asynchronous allows longer distance communication
  Clock skew is not a problem

## Slide 14: UART applications
Used by modems to communicate with network
Computers used to have an RS232 port, standard
Not well used anymore, outside of embedded systems
  Replaced by USB, Ethernet, etc.
Simple, low HW overhead
Build into most microcontrollers

## Slide 15: Serial on Arduino

## Slide 16: Arduino serial communication
UART protocol used over the USB cable
Initialize by using Serial.begin()
Serial.begin(speed) or Serial.begin(speed,config)
  speed is the baud rate
  config sets the data bits, parity, and stop bits
  Serial.begin(9600)
  Serial.begin(9600, SERIAL_8N1)
    8 data bits, no parity bit, and 1 stop bit
Usually call Serial.begin() in the setup function

## Slide 17: Sending text over serial
Use Serial.print() or Serial.println() to print text in the serial monitor
  Strings are converted to ASCII and sent using UART
Serial.println(“Hello World!”);

## Slide 18: Reading data over serial
Data can be sent to the Arduino via the serial monitor
When data is sent, it goes into a buffer in the Arduino until it is read
Serial.available() is used to see how many bytes are waiting in the buffer
  int byteNum = Serial.available();

## Slide 19: Serial.read()
Returns 1 byte from the serial buffer
int bval = Serial.read();
Returns -1 if no data is available
Serial.readBytes() writes several bytes into a buffer
char buff[10];
Serial.readBytes(buff,10);